## Slide 1: AUTOMATIC BLINDS CONTROL SYSTEM
November - 2024
Osama Naji Amr
Emir Ayar
Çağla Kutluk Baydemir

## Slide 2
Contents
Goal of the Project
Electronic Analysis
Mechanical Analysis
MATLAB Results

## Slide 3
The aim is to develop a model of an automated blinds system using a DC motor and implement a PID control scheme. The project will also analyze performance under various conditions.
Key Goals of the Project

## Slide 4: DCX 22 S MODEL
The Maxon DCX 22 S motor is an ideal choice for the automated blinds project because :
it combines compact size, high precision, and efficient performance.
Its ironless winding design allows smooth, continuous motion—important for stable blind operation.
With a torque constant (Kt) of 0.019 Nm/A and a back EMF constant (Ke) of 0.019 V/(rad/s), it works well with the control system requirements in our simulation.
The DCX 22 S's low inertia also enables quick acceleration and deceleration. (very useful in systems like this blinds’ system)

## Slide 5
PARAMETER | VALUE | UNIT
Mass of Blinds | 2.0 | kg
Radius | 0.05 | m
Moment of Inertia | 0.01 | kg·m²
Friction Torque | 0.05 | Nm
Motor Resistance | 1.1 | Ω
Motor Inductance | 0.015 | H
System Components
This table summarizes key mechanical and electrical parameters crucial for the functionality of the automatic blinds control system.

## Slide 6: Modeling Dynamics
The system’s electrical dynamics are captured by a differential equation integrating voltage, resistance, and back EMF, defining current change over time.
(Ke): Back EMF constant
(Rm): Motor resistance
(Lm): Motor inductance
(V): Voltage
(I): Motor current
Electrical Dynamics

## Slide 7: Modeling Dynamics
Mechanical dynamics are described with a second differential equation that relates motor torque and friction to angular acceleration of the blinds.
(m): Mass of blinds
(R): Radius of blinds
(J): Moment of inertia
(τ friction): Friction torque
(Kt): Torque constant
(I): Motor current
(ω): Angular velocity of blinds
Mechanical Dynamics

## Slide 8
Simulation Results

## Slide 9
Simulation Results
Blind Position
Initial motor speed ramps up quickly as the blinds begin to close.
Approaching target speed
Speed oscillates as it stabilizes near the setpoint. (50rad/s)
Stable operation (PID Voltage)
Motor speed remains consistent with minor fluctuations.
Speed Error
Speed error is detected when the motor speed starts drifting away from desired speed. (50rad/s).
Decreased speed due to increased load as blinds fully close.

## Slide 10: PID Control Overview
As shown, an oscillation spike can be seen at the intial voltage due to the PID controller taking some time to start its “controlling effect”. A steady voltage and current are kept to maintain the desired motor speed.(50rad/s).
It may look like the steady voltage is 0 but it is not. A 0V would cause no current through the motor and thus, the motor will stop moving and the blind will not close. A very small voltage value is reasonable though.

## Slide 11: Conclusion & Future Work
The automatic blinds control system successfully integrates PID control for efficiency. Future enhancements may include smart features for improved adaptability.
Summary and Applications

## Slide 12: Questions?

## Slide 13: Thank you for listening